## Slide 1
PART 1
Acoustic Simulation
& Baseline FxLMS
Active Noise Cancellation • Dataset Generation • Baseline Evaluation
Class presentation

## Slide 2
1. Objective and ANC concept
What Part 1 builds and measures
02
Goal
Build a simulated acoustic environment, validate FxLMS, and establish a baseline for faster adaptation methods.
Primary source
Unwanted noise
Error mic
Measures residual
Secondary speaker
Produces anti-noise
Residual error: e(n) = d(n) + yₛ(n)
Objective: minimize mean-square error E[e²(n)]

## Slide 3
2. Acoustic room setup
Simulation parameters based on the stated configuration
03
Room
6 × 6.2 × 3 m
Sampling rate
16 kHz
62.5 μs per sample
RT60
0.15 s
Short reverberation
Impulse response
512 taps = 32 ms
Room reflections are modelled using the Image-Source Method (ISM).

## Slide 4
3. Sources and acoustic paths
Only the primary source moves; speaker and microphone stay fixed
04
Primary source
[1.5, 1, 1] → [3, 2, 2] m
2,048 positions
Secondary speaker
[3, 2.5, 1.5] m
Fixed
Error microphone
[4.5, 3, 1.5] m
Fixed
Primary path P
Noise source → microphone
Secondary path G
Speaker → microphone
Model assumption: Ĝ = G
Perfect secondary-path estimate in this experiment.
P: primary acoustic path G: physical secondary path Ĝ: estimated secondary path

## Slide 5
4. How FxLMS cancels noise
The algorithm accounts for the secondary speaker-to-microphone path
05
Reference noise
x(n): white Gaussian noise
Adaptive filter
y(n) = wᵀ(n)x(n)
Microphone error
e(n) = d(n) + G*y(n)
Primary signal: d(n) = P * x(n)
Filtered reference: x_f(n) = Ĝ * x(n)
Simplified update:
w(n+1) = w(n) + μ e(n) x_f(n)
Your implementation uses a normalized, block-averaged update (Eq. 4).
μ controls adaptation speed and stability.

## Slide 6
5. Pipeline and dataset generation
From acoustic paths to experiments
06
1
ism.py
Room simulation
2
build_paths.py
P, G, Ĝ, positions, Wiener filters
3
tests.py
Validate fast FxLMS
4
sweep_mu.py
Find stable step sizes
5
make_dataset.py
Generate converged filters
6
run_part1.py
50-trial experiments
7
make_figures.py
Plots and PCA
Shipped outputs allow Part 2 and Part 3 to start without rerunning the full pipeline.

## Slide 7
6. What the filter dataset tells us
W.npy stores the converged filter for each source position
07
Dataset shape
2,048 × 512
float32 ≈ 4 MiB
Global PCA
81 components → 99%
32 components → 61%
Local PCA
3 components → 99%
64 neighbouring positions
Interpretation
• The main arrival tap shifts by about 82 samples along the path.
• Neighbouring filters are about 20× closer than random pairs.
• Filters are locally low-dimensional, but the full path forms a curved global manifold.
• This structure may help a future method adapt faster by exploiting nearby filters.

## Slide 8
7. Validation results
Two checks build confidence in the baseline
08
Implementation check
Vectorized block FxLMS matches a sample-wise reference to 2 × 10⁻¹⁶.
This is near double-precision numerical error.
Wiener benchmark
FxLMS attenuation: 15.7 dB
Wiener optimum: 15.8 dB
Median relative filter distance: 3.2%
Conclusion
The implementation reproduces the reference algorithm and converges close to the best linear solution under the stated model.

## Slide 9
8. Baseline experiment design
Measure initial learning and recovery after the source moves
09
Trials
50 independent trials
Duration
400 blocks × 100 samples
6.25 ms per block
Source jump
At block 100
Block 0
Start
Block 100
Source jumps
Block 400
End
Convergence threshold: ρ = 0.4 • Steady-state error: last 40 blocks

## Slide 10
9. Step-size sweep: results
Mean convergence time ± standard deviation; attenuation in dB
10
μ | Initial convergence | After jump | Attenuation
8 | 279 ± 31 blocks | 182 ± 17 blocks | 13.6 ± 0.6 dB
16 | 195 ± 69 blocks | 136 ± 15 blocks | 15.5 ± 0.8 dB
24 | 115 ± 62 blocks | 100 ± 13 blocks | 15.5 ± 0.8 dB
32 | 70 ± 37 blocks | 73 ± 16 blocks | 14.7 ± 2.0 dB
48 | Diverges | Diverges | Unstable
Fastest stable tested setting
μ = 32
Best attenuation among stable rows
μ = 16 or 24 (15.5 dB)

## Slide 11
10. Important limitation: attenuation ceiling
Why the result differs from the paper's reported ≈37 dB
11
Reported paper result
≈37 dB
Our Wiener optimum
≈15.8 dB median
Difference
≈21.2 dB
• 512-tap responses are truncated; the secondary path includes a 74-sample delay.
• Some residual energy cannot be cancelled by the specified finite filter configuration.
• Bandlimiting noise and tapering responses did not remove the discrepancy.
• The exact cause is unresolved; the paper's full setup may differ in an unreported detail.
Keep comparisons fair: use the same acoustic model and evaluation method across algorithms.

## Slide 12
Key takeaways
01
Simulate
Model the room and both acoustic paths.
02
Validate
Check the fast implementation and Wiener benchmark.
03
Measure
Compare speed, stability, and attenuation across μ.
04
Exploit structure
Nearby positions produce similar filters.
05
Set the baseline
μ = 32 is fastest among the tested stable settings.
Part 1 creates the validated reference system for evaluating improvements in Part 3.

## Slide 13
Appendix A — Room, impulse responses & frequency response
Simulation geometry and acoustic paths at 16 kHz
Use this figure to explain the room geometry, the 512-tap responses, and how the paths differ by frequency.
13

## Slide 14
Appendix B — Filter dataset & PCA structure
2,048 converged filters; global versus local dimensionality
Global PCA needs 81 components for 99% variance; locally, 3 components explain 99% across 64 neighbours.
14

## Slide 15
Appendix C — Baseline FxLMS error curves
Mean squared error over 50 trials; source jumps at approximately 0.625 s
Faster step sizes generally settle sooner, while the source jump causes a temporary rise in residual error.
15

## Slide 16
Appendix D — Step-size trade-off
Convergence speed versus steady-state attenuation
μ = 32 is fastest among tested stable settings; μ = 16 and 24 achieve the highest reported attenuation.
16