## Slide 1
Compressing 512-tap adaptive filters into 32-dimensional latent codes
Project evaluation • Group of three
Important: figures supplied here are labelled synthetic smoke-test outputs, not Part 1 measurements.
Part 2 — Latent FxLMS Autoencoders

## Slide 2
1. The problem we are solving
02
• Part 1 produces W: 2,048 filters, each with 512 real-valued taps.
• Storing and working with every tap is high-dimensional.
• Goal: learn a compact 32-value latent code for each filter.
• A decoder maps the 32 values back to a 512-tap filter.
• Part 2 is a representation-learning stage; Part 3 uses the decoder and its derivatives.
Input: W.npy • Expected shape: (2048, 512) Output: trained checkpoints + latent codes + evaluation metrics
One filter = 512 numbers → 32 latent numbers Compression in dimension: 16×

## Slide 3
2. Dataset and source positions
03
• Rows correspond to source-position samples.
• Each row contains a 512-tap filter.
• A position-aware holdout tests generalization to unseen positions.
• Synthetic demo plots are for software smoke-testing only.
Real evaluation must use the actual Part 1 W.npy.

## Slide 4
3. Preprocessing: preserve the filter scale
04
• Load W.npy strictly and check its shape.
• Apply one global max-absolute scale.
• Split by source position: every eighth sample is held out.
• Use the saved scale to return decoded filters to original units.
Why not per-filter scaling? It can hide meaningful differences in filter magnitude.

## Slide 5
4. Model architecture: 512 → 32 → 512
05
Encoder: 512 taps → RFFT (257 complex) → 514 real features → 256 → 32 Decoder: 32 → 256 → 514 → IRFFT → 512 taps

## Slide 6
5. Six variants: what changes between them?
06
AE
Reconstruction MSE
VAE
Reconstruction + Gaussian KL
InfoVAE
Reconstruction + MMD
Each also has a +mixup version: AE+mixup, VAE+mixup, InfoVAE+mixup.
• Mixup adds mixed-filter reconstruction consistency (L_C).
• Mixup also encourages latent linearity (L_z).
• InfoVAE default MMD kernel variance = 0.01; monitor whether it saturates.

## Slide 7
6. Training behaviour and loss
07
• Optimizer: Adam, learning rate 0.001.
• Default research run: up to 120 epochs with early stopping.
• VAE beta = 1; mixup weights = 1.
• Demo: only 8 epochs to smoke-test the pipeline.
A lower training loss alone does not prove better filters.

## Slide 8
7. Does the decoder reconstruct unseen filters?
08
• Held-out positions are not used for training.
• Compare the original and decoded tap sequences.
• Use relative reconstruction error as one metric.
• Check attenuation too—not only visual similarity.
The supplied figure is a synthetic demo, not a real-data result.

## Slide 9
8. Comparing models fairly
09
• Compare mean and median held-out relative error.
• PCA-32 is a simple dimensionality-reduction baseline.
• Choose using held-out reconstruction AND attenuation.
• Do not present synthetic numbers as Part 1 simulation results.

## Slide 10
9. What do the 32-dimensional latent codes show?
10
• Each dot represents one filter's latent code.
• Colour indicates source-position index.
• PCA shows only a 2D view of a 32D code.
• Patterns are exploratory, not proof of performance.

## Slide 11
10. Why use mixup?
11
• Blend two filters using a mixing weight.
• L_C: reconstruct the mixed filter consistently.
• L_z: encourage linearity in latent space.
• Stress-test unseen convex combinations.
Mixup helps test interpolation behaviour; it does not guarantee low reconstruction error.

## Slide 12
11. Baseline: PCA with 32 components
12
• PCA is linear; an autoencoder can learn nonlinear mappings.
• Compare reconstruction error using the same test split.
• Use identical input scaling for a fair comparison.

## Slide 13
12. Decoder Jacobian: bridge to Part 3
13
• Jacobian shape: 512 × 32.
• It is computed by automatic differentiation.
• FFT and inverse FFT are differentiable and have no learned parameters.
• Smooth SiLU activations support derivative-based analysis.

## Slide 14
13. Outputs, limitations, and final takeaway
14
• Outputs: model checkpoints, Z_<model>.npy, z0_<model>.npy, metrics, and plots.
• If P.npy and g.npy are available, evaluate attenuation of decoded filters.
• The attenuation formula follows Part 1: 10 log10(sum(p²) / sum(r²)).
• Paper/project notes report a setup discrepancy: about 15.8 dB median Wiener-optimum in Part 1 versus about 37 dB in the paper.
• Final model selection must use real-data held-out error AND attenuation.
Takeaway: learn a compact 32D representation, validate on unseen positions, and pass a differentiable decoder to Part 3.