## Slide 1
Signals and Systems Project
Active Noise Control using Latent FxLMS
Authors
Navneethnath KT
Sanskar V
Kiran PB
Signals & Systems

## Slide 2: Latent FxLMS
Accelerating active noise control with neural adaptive filters
Signals & Systems course project
Based on Sarkar, Lu, Mittal, Zhuang, Corey & Singer (2025)
Notes: Introduce the paper: Sarkar et al., 2025. Goal: make active noise control adapt faster by searching a small latent space.

## Slide 3: The problem: cancel noise at one spot
Active noise control plays anti-noise so the two sound fields add to zero at an error microphone.
A filter w must be learned on the fly, since rooms and sources change.
Paths are LTI systems: P (noise to mic) and G (speaker to mic).
Goal: g ∗ w ∗ x ≈ −p ∗ x
x[n]
P
W
G
+
e
Ĝ
LMS update
Block diagram of FxLMS (error e feeds the update)
Notes: Superposition: speaker output g*w*x should equal minus p*x at the error microphone.

## Slide 4: FxLMS: the baseline math
Error at the microphone
e = p ∗ x + g ∗ w ∗ x
Filtered reference (estimated path)
x̂ₙ = ĝᵀxₙ = Σ ĝᵢ xₙ₋ᵢ
Normalized LMS update
w[n] = w[n−1] − μ eₙ x̂ₙ / (ε + ‖x̂ₙ‖²)
w_opt
w[n−1]
∇e
−μ∇e
Weight space ℝᴸ (L = 512): each step walks down the error surface
Notes: Walk through the three equations, then the vector picture: the update moves the weight vector against the gradient.

## Slide 5: Novelty: adapt on the manifold
Source moves within a known region, so good filters lie on a low-dimensional manifold.
Learn it with an autoencoder (512 → 32 → 512).
Update z, not w. The decoder D(z) always outputs a plausible filter.
First combination of neural networks with ANC under moving sources.
D(Z): manifold of good filters
Z (latent, k = 32)
z₁
z₂
W₁
W₂
z₂ = z₁ − μ_z∇ₓe
direct step leaves manifold
Weight space ℝ⁵¹²
Notes: Key novelty: adapt in a 32-dim latent space; the decoder guarantees every candidate is a realistic filter.

## Slide 6: Latent FxLMS pipeline
1 · Offline: learn the filter manifold
Converged filters w (512 taps)
RFFT + Encoder E
Latent z (32)
Decoder D
Rebuilt filter ŵ
2 · Online: adapt only z
Error eₙ and x̂ₙ
Gradient eₙx̂ₙ (512-d)
Jacobian Υ (32×512)
Update z (32-d)
w = D(z) to speaker
z[n] = z[n−1] − μ_z Υ(z[n−1]) (eₙ x̂ₙ)
Notes: Two phases: offline training of the autoencoder on converged filters, then online latent updates using the decoder Jacobian.

## Slide 7: Signals & Systems concepts used
Convolution & LTI
e = p∗x + g∗w∗x
Impulse response
FIR filters, L = 512 taps
Sampling
Nyquist-sampled x[n], 16 kHz
Causality
Source must be farther than speaker
Superposition
Anti-noise adds to cancel noise
DFT / RFFT
Filter spectrum feeds the network
Notes: Map each concept to a topic from the course.

## Slide 8: Vector pictures of the key ideas
Mixup: convex combination of filters
γw₁ + (1−γ)w₂, γ ~ U[0,1]
w₁
w₂
mix
Decoder must reproduce the whole segment
Jacobian maps gradient to latent space
ℝ⁵¹² gradient
ℝ³² gradient
Υ
Data-norm: μ_z Υ(eₙx̂ₙ) / (‖x̂ₙ‖²+ε)
Latent-norm: μ_z Υ(eₙx̂ₙ) / (‖Υx̂ₙ‖²+ε)
Notes: Left: mixup trains the autoencoder on convex combinations, which model intermediate filters. Right: Jacobian pushes the gradient into latent space; two normalization options.

## Slide 9: Results: faster, same accuracy
Chart: Convergence time (blocks of 100 samples)
| Unconstrained | InfoVAE | Mixup | VAE+mixup | InfoVAE+mixup
Data-normalized | 63 | 64 | 16 | 21 | 15
Latent-normalized | 20 | 32 | 10 | 24 | 11
≈85 → ≈10
blocks to converge: FxLMS vs best latent model
≈37 dB
steady-state noise reduction; all models within 3 dB
Source: Sarkar et al. (2025), Fig. 7; bar heights read from the chart, approximate. FxLMS ≈ 85 blocks.
Notes: Values are read from Fig. 7 of the paper, so say roughly. Best model: latent-normalized InfoVAE + mixup.

## Slide 10: Real-world applications
Car cabins
Engine, road and tire noise at headrest speakers
Headphones & earbuds
Fast re-adaptation as head or noise moves
Aircraft cabins
Low-frequency propeller and engine drone
Homes & offices
HVAC ducts, appliances, road noise at a window
Industrial booths
Machinery at a known, constrained position
Passing vehicles
Source moves along a known path, like the paper’s line
Notes: Common thread: noise source in a known region, speaker and error mic near the listener.

## Slide 11: Takeaways & limitations
1
Constrain the search
Updating a 32-d latent vector instead of 512 weights speeds up convergence.
2
What worked best
Latent-normalized updates with a mixup-trained decoder; plain VAE did worse.
3
Limits
Simulation only; needs a known source region and a known static secondary path.
Notes: Honest limits: only simulated data, assumes known region and static secondary path.